## Slide 1: Lot 3 - Développements
MNGT to FAC-CM Interface
Version 4
Baris DEMIRAY
Baris.Demiray@eurecom.fr / 04 93 00 82 74
Michelle WETTERWALD
Michelle.Wetterwald@eurecom.fr / 04 93 00 81 31

## Slide 2: Generic Information
For all the packets defined herein,
  Byte-order is Big Endian
  Packet exchange is done through a UDP socket
  Unless stated otherwise there is padding for variable-size fields to make entire packet‘s size multiples of DWORD
  Reserved fields should be zeroed

## Slide 3: Socket Interface
MGMT listens to the port number 1402 (by default) for incoming UDP data
This port number may be altered through the configuration file of MGMT (see SCOREF-MGMT_Configuration.pdf)
FAC shall bind() to a certain port throughout the data exchange, i.e. all the packets should be sent from the same port number

## Slide 4: Message Header
Bit 0: vendor specific or extended message flag (E)
  Used to indicate that a custom message format is used
  For vendor specific extension capabilities
Bit 1: Validity flag (used to indicate of non-existent data)
Version information (4 bits)
Priority (Optional, 3 bits)
Event Type (8 bits)
Event Subtype (8 bits)
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 

## Slide 5: Message type & subtype
Event Type (ET) | Event Sub-type (EST) | Direction | Encoding | Description
ANY |  |  | 0 | Unspecified
 | UNSPECIFIED | Unspecified | 0 | Unspecified
LOCATION |  |  | 1 | Location Event
 | LOCATION_UPDATE | FAC-CMMGMT | 10 | Update EGO Location Position Vector
CONFIGURATION |  |  | 3 | Configuration Event
 | CONFIGURATION_UPDATE_AVAILABLE | FAC-CMMGMT | 0 | Indication: New configuration available
 | CONFIGURATION_REQ | FAC-CMMGMT | 11 | Configuration Request
 | CONFIGURATION_RES_CONT | FAC-CMMGMT | 12 | Configuration Request Continuous mode
 | CONFIGURATION_RES_BULK | FAC-CMMGMT | 13 | Configuration Request Bulk mode
 | CONFIGURATION_NOTIFICATION | FAC-CMMGMT | 14 | Configuration Notification
 | COMM_PROF_REQ | FAC-CMMGMT | 15 | Communication Profile Table Request
 | COMM_PROF_REP | FAC-CMMGMT | 16 | Communication Profile Table Response
 | COMM_PROF_SELECTION_REQ | FAC-CMMGMT | 17 | Communication Profile Selection Request
 | COMM_PROF_SELECTION_RES | FAC-CMMGMT | 18 | Communication Profile Selection Response

## Slide 6: Location

## Slide 7: Location Update
Location Update is sent from FACilities to MGMT
Carries position vector
All position vector fields are described in 102 636-4-1
  Timestamp (ms) = Timestamp(UET)mod2^32
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 |  | 3 | 4 | 5 |  | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  |  |  | 
Timestamp |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Latitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Longitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Speed |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Heading |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Altitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | TAcc |  |  |  | PodAcc |  |  |  | SAcc |  |  | Hacc |  |  |  | AltAcc |  | 

## Slide 8: Configuration

## Slide 9: Configuration Available Event
Is used to notify clients of MGMT of
  available configurations
  configuration changes
Key count indicates the number of configuration keys available/changed relevant to the recipient (server always provides this info, but client can ignore this field if it is not required)
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Reserved |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Key count (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 10: Configuration Request
Is used to request MGMT to initiate transmission of a configuration
  Request single key: continuous transmission mode and conf-id
  Request all configuration groups: 0xFFFF as conf-id
  Request NET layer configuration group: 0xAAAA as conf-id
  Request FAC layer configuration group: 0xBBBB as conf-id
Transmission mode flag:
  0 for continuous transmission mode (default): each key is wrapped in its own message
  1 for bulk mode: all-in-1 data blob (a single big message containing all keys)
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Conf ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Trasmission Mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 11: Configuration Response Continuous
Is used to declare configuration parameters
ConfID is mapped to name of configuration parameter
Encoding of ConfValue determined by Conf-ID
Size of ConfValue is indicated in Length
  Field: Length (bytes 6+7) -> is mandatory. Length indicates DWORD-length of „Conf Value“, e.g. Length=2 means ConfValue is actually 8 bytes long
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Conf ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Length |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf Value (of size ‘Length’) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Notes: Field: Length (bytes 6+7) -> is mandatory. Length indicates DWORD-length of „Conf Value“, e.g. Length=2 means ConfValue is actually 8 bytes long.

## Slide 12: Configuration Response Bulk
Bulk transfer message incorporates „Key Count“ number of configuration items
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
reserved |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Key count |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Length (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf Value |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Length (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf Value |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
... (continues up to „key count“) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 13: Configuration Notification
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Conf ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Length |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf Value (of size ‘Length’) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Configuration Notification is used to keep MGMT up to date in case of a configuration change in another module
There is no continuous version of this message, a single message is goint to be sent for every change
`Length’ field denotes number of bytes (not DWORDS as in Configuration Response Continuous message)
String values are not NULL-terminated, `Length’ field should help to parse it properly
Notes: Field: Length (bytes 6+7) -> is mandatory. Length indicates DWORD-length of „Conf Value“, e.g. Length=2 means ConfValue is actually 8 bytes long.

## Slide 14: Communication Profile

## Slide 15: Communication Profile Request
This packet allows sender to ask either all or a subset of the communication profile table by setting all filter fields to 0xff, or by setting relevant bitmap fields to 1, respectively
Transport: |BTP_A|BTP_B|TCP|UDP|RTP|STCP|Res|Res|
Network: |GN|IPv6_GN|IPv6|IPv4| IPv4/v6 |DSMIPv4/v6|Res|Res|
Access: |ITSG5|3G|11n|Ethernet|Res|Res|Res|Res|
Channel: |CCH|SCH1|SCH2|SCH3|SCH4|Res|Res|Res|
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Transport |  |  |  |  |  |  |  | Network |  |  |  |  |  |  |  | Access |  |  |  |  |  |  |  | Channel |  |  |  |  |  |  | 

## Slide 16: Communication Profile Response
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
CP Count |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  | 
Communication Profile ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Transport |  |  |  |  |  |  |  | Network |  |  |  |  |  |  |  | Access |  |  |  |  |  |  |  | Channel |  |  |  |  |  |  | 
... (continues up to „CP Count“) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
This packet contains those communication profiles asked through sending a Communication Profile Request
Indexes of the bitmaps are the same and given in the next page

## Slide 17: Communication Profile Response
Transport | Network | Access | Channel
BTP_A = 0x1 BTP_B = 0x2 TCP = 0x3 UDP = 0x4 RTP = 0x5 STCP = 0x6 | GN = 0x1 IPv6_GN = 0x2 IPv6 = 0x3 IPv4 = 0x4 IPv4/v6 = 0x5 DSMIPv4/v6 = 0x6 | ITSG5 = 0x1 3G = 0x2 11n = 0x3 Ethernet = 0x4 | CCH = 0x1 SCH1 = 0x2 SCH2 = 0x3 SCH3 = 0x4 SCH4 = 0x5
Index numbers for protocols are as follows,

## Slide 18: Communication Profile Selection Request
This packet allows MGMT client to ask for a suitable communication profile according to its requirements expressed in,
Latency
Relevance
Reliability
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Latency |  |  |  |  |  |  |  | Relevance |  |  |  |  |  |  |  | Reliability |  |  |  |  |  |  |  | reserved |  |  |  |  |  |  | 

## Slide 19: Communication Profile Selection Response
The response allows MGMT to offer a communication profile based on the criteria given by client
Request parameters latency, relevance, reliability, and are sent back to let MGMT client match requests and relevant responses
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Latency |  |  |  |  |  |  |  | Relevance |  |  |  |  |  |  |  | Reliability |  |  |  |  |  |  |  | reserved |  |  |  |  |  |  | 
Communication Profile ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 20: FAC Group Configuration Keys
ITS KEY NAME | CONF ID | DESCRIPTION / VALUES
itsStationType | 0 | See PREDRIVE VehicleType list for info (default: 1=CAR, or 30=RSU)
itsStationSubType | 1 | 0=public, 1=private
itsVehicleWidth | 2 | scale 0,1m, max 63
itsVehicleLength | 3 | scale 0,1m, max 1023
CAM BTP Port | 3010 | Unsigned integer 0 - 65535
DENM BTP Port | 3011 | Unsigned integer 0 - 65535
LDM Garbage Collection Interval | 3020 | Unsigned integer [ms]