## Slide 1: Lot 3 - Développements
MNGT To FAC-CM Interface
Version 1

## Slide 2: Message Header
Bit 0: vendor/extended msg flag (E)
  Used to indicate that a custom message format is used
  For vendor specific extension capabilities
Bit 1: Validity flag (used to indicate of non-existent data)
Version information (4 bits)
Priority (Optional, 3 bits)
Event Type (8 bits)
Event Subtype (8 bits)
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 

## Slide 3: Message type & subtype
Event Type (ET) | Event Sub-type (EST) | Direction | Encoding | Description
ANY |  |  | 0 | Unspecified
 | UNSPECIFIED | Unspecified | 0 | Unspecified
LOCATION |  |  | 1 | Location Event
 | LOCATION _TABLE_REQ | FAC-CMMGMT | 3 | Location Table Request
 | LOCATION _TABLE_RES | FAC-CMMGMT | 4 | Location Table Response
CONFIGURATION |  |  | 3 | Configuration Event
 | CONFIGURATION_UPDATE_AVAILABLE | FAC-CMMGMT | 0 | Indication: New configuration available
 | CONFIGURATION_REQ | FAC-CMMGMT | 11 | Configuration Request
 | CONFIGURATION_RES_CONT | FAC-CMMGMT | 12 | Configuration Request Continuous mode
 | CONFIGURATION_RES_BULK | FAC-CMMGMT | 13 | Configuration Request Bulk mode
 | COMM_PROF_REQ | FAC-CMMGMT | 14 | Communication Profile Table Request
 | COMM_PROF_REP | FAC-CMMGMT | 15 | Communication Profile Table Response
 | COMM_PROF_SELECTION_REQ | FAC-CMMGMT | 16 | Communication Profile Selection Request
 | COMM_PROF_SELECTION_RES | FAC-CMMGMT | 17 | Communication Profile Selection Response

## Slide 4: Location

## Slide 5: Location Update
Update Position Event is sent from MGMT component to FAC
Carries node’s position vector
All position vector fields are described in 102 636-4-1
  Timestamp (ms) = Timestamp(UET)mod2^32
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 |  | 3 | 4 | 5 |  | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  |  |  | 
Timestamp |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Latitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Longitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Speed |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Heading |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Altitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | TAcc |  |  |  | PodAcc |  |  |  | SAcc |  |  | Hacc |  |  |  | AltAcc |  | 

## Slide 6: Location Table Request
Queries the location table for the position vector of a node, given by its GN_Addr
Query location event generates a Update Location Event.
  All Location Table can be requested by setting a GN_ADDR with all bytes set to 0xFF
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
GN_ADDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 7: Location Table Response
First entry is always EGO vehicle.
Network Flags: TBD
LVP Flags: | is_neighbour (0/1) | is_pending (0/1) | RES | RES | RES | RES | RES | RES |
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 |  | 3 | 4 | 5 |  | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  |  |  | 
LPV Count |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Network Flags |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  |  |  | 
GN_ADDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Timestamp |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Latitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Longitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Speed |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Heading |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Altitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | TAcc |  |  |  | PodAcc |  |  |  | SAcc |  |  | Hacc |  |  |  | AltAcc |  | 
Sequence Number |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | LPV Flags |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  |  |  | 
... (continues up to „LPV count“) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 8: Configuration

## Slide 9: Configuration Available Event
Used to notify clients of ITS MGMT of
  available configurations
  configuration changes
Key count indicates the amount of configuration keys available for this client (server always provides this info, but client can ignore this field if this info is not required)
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Reserved |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Key count (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 10: Configuration Request
Used to request MGMT to initiate transmission of a configuration
  Request single key: continuous transmission mode and conf-id
  Request all configuration groups: 0xFFFF as conf-id
  Request NET layer configuration group: 0xAAAA as conf-id
  Request FAC layer configuration group: 0xBBBB as conf-id
Transmission mode flag:
  0 for continuous transmission mode (default): each key is wrapped in its own message
  1 for bulk mode: all-in-1 data blob (a single big message containing all keys)
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Conf ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Trasmission Mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 11: Configuration Response Continuous
Used to set configuration parameters
ConfID is mapped to name of configuration parameter
Encoding of integer ConfValue determined by Conf-ID
Size of ConfValue is indicated in Length
  Field: Length (bytes 6+7) -> is mandatory. Length indicates DWORD-length of „Conf Value“, e.g. Length=2 means ConfValue is actually 8 bytes long
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Conf ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Length |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf Value |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Notes: Field: Length (bytes 6+7) -> is mandatory. Length indicates DWORD-length of „Conf Value“, e.g. Length=2 means ConfValue is actually 8 bytes long.

## Slide 12: Configuration Response Bulk
Bulk transfer message incorporates as many configuration item as indicated by „Key Count“ field
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
reserved |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Key count |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Length (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf Value |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Length (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf Value |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
... (continues up to „key count“) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 13: Communication Profile Request
The request allows to filter part of the communication profile table setting the bit to 1 where necessary.
Transport: |BTP_A|BTP_B|TCP|UDP|RTP|STCP|Res|Res|
Network: |GN|IPv6_GN|IPv6|IPv4| IPv4/v6 |DSMIPv4/v6|Res|Res|
Access: |ITSG5|3G|11n|Ethernet|Res|Res|Res|Res|
Channel: |CCH|SCH1|SCH2|SCH3|SCH4|Res|Res|Res|
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Transport |  |  |  |  |  |  |  | Network |  |  |  |  |  |  |  | Access |  |  |  |  |  |  |  | Channel |  |  |  |  |  |  | 

## Slide 14: Communication Profile Response
Transport | Network | Access | Channel
BTP_A = 0x1 BTP_B = 0x2 TCP = 0x3 UDP = 0x4 RTP = 0x5 STCP = 0x6 | GN = 0x1 IPv6_GN = 0x2 IPv6 = 0x3 IPv4 = 0x4 IPv4/v6 = 0x5 DSMIPv4/v6 = 0x6 | ITSG5 = 0x1 3G = 0x2 11n = 0x3 Ethernet = 0x4 | CCH = 0x1 SCH1 = 0x2 SCH2 = 0x3 SCH3 = 0x4 SCH4 = 0x5
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
CP Count |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  | 
Communication Profile ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Transport |  |  |  |  |  |  |  | Network |  |  |  |  |  |  |  | Access |  |  |  |  |  |  |  | Channel |  |  |  |  |  |  | 
... (continues up to „CP Count“) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 15: Communication Profile Selection Request
The request allows MGMT client to select a communication profile according to its needs listed below,
Latency
Relevance
Reliability
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Latency |  |  |  |  |  |  |  | Relevance |  |  |  |  |  |  |  | Reliability |  |  |  |  |  |  |  | reserved |  |  |  |  |  |  | 

## Slide 16: Communication Profile Selection Response
The response allows MGMT to offer a communication profile based on the criteria set by client
Request parameters latency, relevance, reliability, and are sent back to let MGMT client match requests and relevant responses
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Latency |  |  |  |  |  |  |  | Relevance |  |  |  |  |  |  |  | Reliability |  |  |  |  |  |  |  | Communication Profile ID |  |  |  |  |  |  | 

## Slide 17: FAC Group Configuration Keys
ITS KEY NAME | CONF ID | DESCRIPTION / VALUES
itsStationType | 0 | See PREDRIVE VehicleType list for info (default: 1=CAR, or 30=RSU)
itsStationSubType | 1 | 0=public, 1=private
itsVehicleWidth | 2 | scale 0,1m, max 63
itsVehicleLength | 3 | scale 0,1m, max 1023
CAM BTP Port | 3010 | Unsigned integer 0 - 65535
DENM BTP Port | 3011 | Unsigned integer 0 - 65535
LDM Garbage Collection Interval | 3020 | Unsigned integer [ms]