## Slide 1: Lot 3 - Développements
MNGT To CM-GN Interface

## Slide 2: Message Header
Bit 0: vendor/extended msg flag (E)
  Used to indicate that a custom message format is used
  For vendor specific extension capabilities
Bit 1: Validity flag (used to indicate of non-existent data)
Version information (4 bits)
Priority (Optional, 3bits)
Event Type (8 bits)
Event Subtype (8 bits)
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 

## Slide 3: Message type & subtype
Event Type (ET) | Event Sub-type (EST) | Direction | Encoding | Description
ANY |  |  | 0 | Unspecified
 | UNSPECIFIED | Unspecified | 0 | Unspecified
LOCATION |  |  | 1 | Location Event
 | LOCATION_UPDATE | GN-CMMGMT | 0 | Update EGO Location Position Vector
 | LOCATION _TABLE_REQ | GN-CMMGMT | 1 | Location Table Request
 | LOCATION _TABLE_RES | GN-CMMGMT | 2 | Location Table Response
CONFIGURATION |  |  | 3 | Configuration Event
 | CONFIGURATION_UPDATE_AVAILABLE | GN-CMMGMT | 0 | Indication: New configuration available
 | CONFIGURATION_REQ | GN-CMMGMT | 1 | Configuration Request
 | CONFIGURATION_RES_CONT | GN-CMMGMT | 2 | Configuration Request Continuous mode
 | CONFIGURATION_RES_BULK | GN-CMMGMT | 3 | Configuration Request Bulk mode
 | COMM_PROF_REQ | GN-CMMGMT | 4 | Communication Profile Table Request
 | COMM_PROF_REP | GN-CMMGMT | 5 | Communication Profile Table Response
STATE |  |  | 4 | State Event
 | WIRELESS_STATE_REQ | GN-CMMGMT | 2 | Wireless State Event Request
 | WIRELESS_STATE_RES | GN-CMMGMT | 3 | Wireless State Event Response
 | NETWORK_STATE | GN-CMMGMT | 4 | Network State Event

## Slide 4: Location

## Slide 5: Location Update
Update Position Event sent from MGMT component to GN
Carries node’s position vector
All position vector fields are described in 102 636-4-1
  Timestamp (ms) = Timestamp(UET)mod2^32
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 |  | 3 | 4 | 5 |  | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  |  |  | 
Timestamp |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Latitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Longitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Speed |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Heading |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Altitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | TAcc |  |  |  | PodAcc |  |  |  | SAcc |  |  | Hacc |  |  |  | AltAcc |  | 

## Slide 6: Location Table Request
Queries the location table for the position vector of a node, given by its GN_Addr
Query location event generates a Update Location Event.
  All Location Table can be requested by setting a GN_ADDR with all bytes set to 0xFF
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
GN_ADDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 7: Location Table Response
First entry is always EGO vehicle.
Network Flags: TBD
LVP Flags: | is_neighbour (0/1) | is_pending (0/1) | RES | RES | RES | RES | RES | RES |
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 |  | 3 | 4 | 5 |  | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  |  |  | 
LPV Count |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Network Flags |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  |  |  | 
GN_ADDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Timestamp |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Latitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Longitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Speed |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Heading |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Altitude |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | TAcc |  |  |  | PodAcc |  |  |  | SAcc |  |  | Hacc |  |  |  | AltAcc |  | 
Sequence Number |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | LPV Flags |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  |  |  | 
... (continues up to „LPV count“) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 8: Configuration

## Slide 9: Configuration Available Event
Used to notify clients of ITS MGMT of
  available configurations
  configuration changed
Key count indicates the amount of configuration keys available for this client (server always provides this info, but client can ignore this field if this info is not required)
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Reserved |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Key count (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 10: Configuration Request
Used to request MGMT to initiate transmission of a configuration
  Request single key: continuous transmission mode and conf-id
  Request all configuration groups: OxFFFF as conf-id
  Request NET layer configuration group: 0xAAAA as conf-id
  Request FAC layer configuration group: 0xBBBB as conf-id
Transmission mode flag:
  0 for continuous transmission mode: each key is wrapped in its own msg, default
  1 for bulk mode: all-in-1 data blob (a single big message containing all keys)
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Conf ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | trasmission mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 11: Configuration Response Continous
Used to set configuration parameters
ConfID is mapped to name of configuration parameter
Encoding of ConfValue determined by Conf-ID, default: integer
Size of ConfValue is indicated in Length
  Field: Length (bytes 6+7) -> is mandatory. Length indicates DWORD-length of „Conf Value“, e.g. Length=2 means ConfValue is actually 8 bytes long.
“continuous transmission” mode
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Conf ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Length |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf Value |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Notes: Field: Length (bytes 6+7) -> is mandatory. Length indicates DWORD-length of „Conf Value“, e.g. Length=2 means ConfValue is actually 8 bytes long.

## Slide 12: Configuration Response Bulk
bulk transfer mode
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
reserved |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Key count |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Length (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf Value |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Length (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conf Value |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
... (continues up to „key count“) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 13: NET Group Configuration Keys
ITS KEY NAME | CONF ID | DESCRIPTION / VALUES
itsStationType | 0 | See PREDRIVE VehicleType list for info (default: 1=CAR, or 30=RSU)
itsStationSubType | 1 | 0=public, 1=private
itsGnLocalAddrConfMethod | 1000 | 0=auto, 1=managed
itsGnDefaultHopLimit | 1001 | Default Hop Limit (0-255)
itsGnMaxPktLifetime | 1002 | Upper Limit of Packet Lifetime (1-6300000) [ms]
itsGnMinPktRepetitionInterval | 1003 | Lower Limit of the Packet Repetition Interval [ms]
itsGnGeoBcastForwardingAlg | 1010 | 0: Unspecified, 1: Simple, 2 Advanced (optional)
itsGnGeoUcastForwardingAlg | 1011 | 0: Unspecified, 1: Greedy, 2: ETSI-CBF, 3: Revised-CB
itsGnTrafficClassRelevance | 1020 | 0-7 [High 0 <--> 7 Low]
itsGnTrafficClassReliability | 1021 | 0-3 [High 0 <--> 3 Low]
itsGnTrafficClassLatency | 1022 | 0-3 [Low 0 <--> 3 High]
itsGnCbfMinTTS | 1030 | Minimum time-to-send [ms]
itsGnCbfMaxTTS | 1031 | Maximum time-to-send [ms]
itsGnMaxCommRange | 1040 | Theoretical radio communication range [m]
itsGnDefTxPower | 1050 | TxPower [in 1dBm steps]
itsGnDefBitrate | 1051 | Bitrate [in Mbps -- 3, 4.5, 6, 9, 12, 18, 24, 27]
itsGnDefChannel | 1052 | Channel number [176, 178, 180]
itsGnDefPriority | 1053 | Priority [0-7]
itsGnDefChannelBW | 1054 | BandWidth [MHz]
itsSecAllowUnsecure | 2000 | 0=security OFF, 1=security ON
itsSecEnd2End | 2001 | 0=disabled, 1=enabled
itsSecPseudonym | 2002 | 0=disabled, 1=enabled

## Slide 14: Communication Profile Request
The request allows to filter part of the communication profile table setting the bit to 1 where necessary.
Transport: |BTP_A|BTP_B|TCP|UDP|RTP|STCP|Res|Res|
Network: |GN|IPv6_GN|IPv6|IPv4| IPv4/v6 |DSMIPv4/v6|Res|Res|
Access: |ITSG5|3G|11n|Ethernet|Res|Res|Res|Res|
Channel: |CCH|SCH1|SCH2|SCH3|SCH4|Res|Res|Res|
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Transport |  |  |  |  |  |  |  | Network |  |  |  |  |  |  |  | Access |  |  |  |  |  |  |  | Channel |  |  |  |  |  |  | 

## Slide 15: Communication Profile Response
Transport:
  BTP_A = 0x1
  BTP_B = 0x2
  TCP = 0x3
  UDP = 0x4
  RTP = 0x5
  STCP = 0x6
Network:
  GN = 0x1
  IPv6_GN = 0x2
  IPv6 = 0x3
  IPv4 = 0x4
  IPv4/v6 = 0x5
  DSMIPv4/v6 = 0x6
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
CP Count |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  | 
Communication Profile ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Transport |  |  |  |  |  |  |  | Network |  |  |  |  |  |  |  | Access |  |  |  |  |  |  |  | Channel |  |  |  |  |  |  | 
... (continues up to „CP Count“) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Access:
  ITSG5 = 0x1
  3G = 0x2
  11n = 0x3
  Ethernet = 0x4
Channel:
  CCH = 0x1
  SCH1 = 0x2
  SCH2 = 0x3
  SCH3 = 0x4
  SCH4 = 0x5

## Slide 16: State

## Slide 17: Wireless State Request
It contains only the Header.
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 

## Slide 18: Wireless State Response
The response contains all the Wireless Interfaces
The message can be unsolicited if major change
Access Technology
  consistent with widely used NAS-Port-Type http://www.iana.org/assignments/radius-types/radius-types.xml#radius-types-13
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
IF Count |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  | 
Interface ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Access Technology |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Channel Frequency |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Bandwidth |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Channel Busy Ratio |  |  |  |  |  |  |  | Status |  |  |  |  |  |  |  | Average TX Power |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  | 
... (continues up to „IF Count“) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 19: Network State Event
Periodically generated information about the status of the network layer
Default every 10 seconds, used as a heartbeat. The timer can be set by appropriate configuration value
ToUpperLayerPackets – all packets send to GNBTPAPI
Discarded packets – possible reasons are duplicate, error in header, verification failed and other
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
RxPackets |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RxBytes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TxPackets |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TxBytes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ToUpperLayerPackets |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DiscardedPackets |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DuplicatePackets |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ForwardedPackets |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 20: Extension to FAC-CM

## Slide 21: FAC Group Configuration Keys
ITS KEY NAME | CONF ID | DESCRIPTION / VALUES
itsStationType | 0 | See PREDRIVE VehicleType list for info (default: 1=CAR, or 30=RSU)
itsStationSubType | 1 | 0=public, 1=private
itsVehicleWidth | 2 | scale 0,1m, max 63
itsVehicleLength | 3 | scale 0,1m, max 1023
CAM BTP Port | 3010 | Unsigned integer 0 - 65535
DENM BTP Port | 3011 | Unsigned integer 0 - 65535
LDM Garbage Collection Interval | 3020 | Unsigned integer [ms]