## Slide 1: Lot 3 - Développements
MNGT to LTE-CM Interface
Version 1
Baris DEMIRAY
Baris.Demiray@eurecom.fr / 04 93 00 82 74
Michelle WETTERWALD
Michelle.Wetterwald@eurecom.fr / 04 93 00 81 31

## Slide 2: Generic Information
For all the packets defined herein,
  Byte-order is Big Endian
  Packet exchange is done through a UDP socket
  Unless stated otherwise there is padding for variable-size fields to make entire packet‘s size multiples of DWORD
  Reserved fields should be zeroed

## Slide 3: Socket Interface
MGMT listens to the port number 1402 (by default) for incoming UDP data
This port number may be altered through the configuration file of MGMT (see SCOREF-MGMT_Configuration.pdf)
LTE-CM shall bind() to a certain port throughout the data exchange, i.e. all the packets should be sent from the same port number

## Slide 4: Message Header
Bit 0: vendor specific or extended message flag (E)
  Used to indicate that a custom message format is used
  For vendor specific extension capabilities
Bit 1: Validity flag (used to indicate of non-existent data)
Version information (4 bits)
Priority (Optional, 3 bits)
Event Type (8 bits)
Event Subtype (8 bits)
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 

## Slide 5: Message type & subtype
Event Type (ET) | Event Sub-type (EST) | Direction | Encoding | Description
ANY |  |  | 0 | Unspecified
 | UNSPECIFIED | Unspecified | 0 | Unspecified
STATE |  |  | 4 | State Event
 | WIRELESS_STATE_REQ | GN-CMMGMT | 2 | Wireless State Event Request
 | WIRELESS_STATE_RES | GN-CMMGMT | 23 | Wireless State Event Response

## Slide 6: State

## Slide 7: Wireless State Request
It contains only the Header.
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 

## Slide 8: Wireless State Response
The response contains all the Wireless Interfaces
The message can be unsolicited if major change
Abbreviations
RSRP: Reference Signal Received Power
RSRQ: Reference Signal Received Quality
QCI: Channel Quality Indication
0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
E | V | R | R | Version |  |  |  | Priority |  |  | R | R | R | R | R | Event Type |  |  |  |  |  |  |  | Event Subtype |  |  |  |  |  |  | 
Interface ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  | 
Reference Signal Received Power |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Reference Signal Received Quality |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Channel Quality Indication |  |  |  |  |  |  |  | Status |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  |  | Reserved |  |  |  |  |  |  | 
Packet Loss Rate |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |